lil CPU
32 bit instruction.
up to 16 bit data
	Byte	Byte
AX	AL	AH	Accumulator
BX	BL	BH	Base
CX	CL	CH	Count
DX	DL	DH	Data
	SP		Stack Pointer
	BP		Base Pointer
	IP		Instruction Pointer
	FLAGS		Status Flags

Table 1: Register Model

16-Bit (W = 1)		8-Bit (W = 0)
000	AX	0	AL
001	BX	1	BL
010	CX	10	CL
011	DX	11	DL
100	SP	100	AH
101	BP	101	BH
110	IP	110	CH
111	FLAGS	111	DH

# Memory Organization
Total of 17-Bit Adress and 16-Bit Data
Base Pointer:
From:	00000h
To:	0FFFFh
Stack Pointer:
From:	10000h
To:	1FFFFh
# Instruction Set Overview
Instruction Code				Description
Byte 4	Byte 3	Byte 2	Byte 1
7 6 5 4 3 2 1 0	7 6 5 4 3 2 1 0	7 6 5 4 3 2 1 0	7 6 5 4 3 2 1 0
Data Transfer
0 0 0 0 0 0 0 1	W 0 0 0 0 reg[1]	Data if w=1	Data	MOV Immediate to Register
0 0 0 0 0 0 1 0	W d[2] reg1 reg2			MOV Register to Register
0 0 0 0 0 0 1 1	W d 0 0 0 reg	Address high	Address low	MOV Memory from/to Register
0 0 0 0 0 1 0 0	W 0 0 0 0 reg			MOV Register to Memory
0 0 0 0 0 1 0 1				PUSH from Register/Memory
0 0 0 0 0 1 1 0	W 0 0 0 0 reg			PUSH from Register
0 0 0 0 0 1 1 1				POP to Register/Memory
0 0 0 0 1 0 0 0				POP to Register
0 0 0 0 1 0 0 1				Input from port
0 0 0 0 1 0 1 0				Output to port
0 0 0 0 1 0 1 1				PUSHF Push Flags
0 0 0 0 1 1 0 0				POPF Pop Flags
Arithmetic
0 0 0 0 1 1 0 1	W d reg1 reg2			ADD (Unsigned)
0 0 0 0 1 1 1 0	W 0 0 0 0 reg	Data if w=1	Data	ADD Immediate
0 0 0 0 1 1 1 1				ADD to Reg
0 0 0 1 0 0 0 1				ADD to Stack
0 0 0 1 0 0 1 0				ADD to Memory
0 0 0 1 0 0 1 1				IADD Integer Add (Signed)
0 0 0 1 0 1 0 0				INC
0 0 0 1 0 1 0 1				SUB (Unsigned)
0 0 0 1 0 1 1 0				ISUB Integer Subtract (Signed)
0 0 0 1 0 1 1 1				DEC
0 0 0 1 1 0 0 0				NEG = change sign
				MUL = Multiply (Unsigned)
				IMUL integer Multiply (Signed)
				DIV Divide (Unsigned)
				IDIV Integer Divide (Signed)
Logic
				Shift right
				Shift left
				Rotate right
				Rotate left
				Rotate Throug Carry flag left
				Rotate Throug Carry flag right
				NOT
				AND
				OR
				XOR
STRING MANIPULATION
				REP e Repeat
				MOVS Move Byte/Word
				CMPS Compare Byte/Word
				SCAS Scan Byte/Word
				LODS Load Byte/Word to AL/AX
				STOS Store Byte/Word from AL/AX
CONTROL TRANSFER
				JMP Unconditional Jump
				JE/JZ Jump on Equal/Zero
				JL/JNGE Jump on Less/Not Greater / or Equal
				JLE/JNG Jump on Less or Equal/ / Not Greater
				JB/JNAE Jump on Below/Not Above / or Equal
				JBE/JNA Jump on Below or Equal/ / Not Above
				JO Jump on Overflow
				JS Jump on Sign
				JNE/JNZ e Jump on Not Equal/Not Zero
				JNL/JGE e Jump on Not Less/Greater / or Equal
				JNLE/JG e Jump on Not Less or Equal/ / Greater
				JNB/JAE e Jump on Not Below/Above / or Equal
				JNBE/JA e Jump on Not Below or / Equal/Above
				JNP/JPO e Jump on Not Par/Par Odd
				JNO e Jump on Not Overflow
				JNS e Jump on Not Sign
PROCESSOR CONTROL
				WAIT
				HLT Halt
[1] reg is always 3 bit for Selection of Regisers
[2] d = 0 from reg1 to reg2 - d = 1 from reg2 to reg1